## Slide 1: Supporting Industry 4.0 in Next-generation Cellular: The Digital Twin Use Case
Carla Fabiana Chiasserini, Politecnico di Torino
https://www.telematica.polito.it/member/carla-fabiana-chiasserini/
R2T2 2021

## Slide 2: 1
New-generation cellular

## Slide 3: What is/was a breakthrough in 5G?
Vertical industries become customers of mobile networks
Verticals specify their quality of service requirements (not limited to data rate any longer)
Source: IMT vision Recommendation ITU-R M.2083-0

## Slide 4
How is it possible to host vertical services with ultra low (UL) latency?

## Slide 5: How is it possible to host vertical services with UL latency? First, network as a programmable platform
Edge computing: the network as a programmable platform
Network will process and store data, not just transfer it
Processing and applications within the network to provide mobile users with services
Lower delays and higher efficiency

## Slide 6
Simple forwarding HW
Simple forwarding HW
Simple forwarding HW
Simple forwarding HW
Controller/Network OS
Southbound interface: HW open interface
Northbound interface: Network control API
Capone – Netsoft 2015
Physical infrastructure
How is it possible to host vertical services with UL latency? First, network as a programmable platform
SDN as a key technology

## Slide 7
Management and Orchestration MANO
Virtual Functions VNFs
Service
NFV World Congress - OSM
How is it possible to host vertical services with UL latency? Second, service virtualization

## Slide 8: NFV, SDN, MANO: ETSI Architectural view
Computing
Storage
Network
Hardware Resources
Virtual Computing
Virtual Storage
Virtual Network
Virtualization @ SDN Controller
NFVI
Virtual Infrastructure Manager (VIM)
VNF/VA Manager
NFV Orchestrator
VNF
VNF
VNF
VNF
VNF
MANO
Verticals
OSS/BSS
SDN world
Service
Physical
resources

## Slide 9: NFV, SDN, MANO: ETSI Architectural view
Computing
Storage
Network
Hardware Resources
Virtual Computing
Virtual Storage
Virtual Network
Virtualization @ SDN Controller
NFVI
Virtual Infrastructure Manager (VIM)
VNF/VA Manager
NFV Orchestrator
VNF
VNF
VNF
VNF
VNF
MANO
Verticals
OSS/BSS
SDN world
Service
Physical
resources

## Slide 10: How is this possible to host vertical services with UL latency? First, network as a programmable platform
Edge computing: the network as a programmable platform
Network will process and store data, not just transfer it
Processing and applications within the network to provide mobile users with services
Lower delays and higher efficiency

## Slide 11
How is it possible to host vertical services, each with the required quality of service (QoS)?

## Slide 12: How is it possible to host vertical services each with the required QoS? Network slicing
Virtualization allows to slice the network into virtual subnetworks (separated sets of resources)
Service deployment = Creating a slice hosting the virtual function set

## Slide 13: Use Case: Digital Twin
Digital Twin app
Interface
Coordinates
Commands
EDGE NETWORK
Drivers
Motion planning
Control
Radio Access Network
VNF 2
target latency: 60 ms
VNF 1 target latency: 600 ms

## Slide 14: Challenges
Vertical service deployment (VNF placement and resource allocation) ⎯ yet lots to learn, especially in presence of dynamic conditions
Virtualization at the Edge poses a performance issue, especially in terms of latency (strict delay constraints), and a cost issue - big concern for Verticals and Mobile Operators
End-to-end slicing

## Slide 15: 2
End-to-end slicing

## Slide 16: Industry 4.0: Digital Twin
Is VERTICAL service virtualization the only one that matters?

## Slide 18: vRAN
Chang et al. RAN Runtime Slicing System for Flexible and Dynamic Service Execution Environment. IEEE Access 6, 34018–34042, and Schmidt et al. Radio Access Network Slicing System, Eurecom

## Slide 19: Possible approaches
AIML-based approaches for allocation of (all types) of resources, i.e., E2E slice configuration:
  centralized (coarse) resource allocation
  distributed fine tuning
Network edge as set of distributed entities:
  centralized ML architectures
  distributed ML architectures

## Slide 20: O-RAN

## Slide 21: Recent work
S. Tripathi, C. Puligheddu, C. Chiasserini, An RL Approach to Radio Resource Management in Heterogeneous Virtual RANs, IEEE WONS 2021
Vrain by NEC et al.
ML-based settings of an LTE vRAN (srsLTE) accounting for CPU consumption
CAREM: ML-based, application-aware management of multiple links* through vRAN
Edge-controlled or edge-assisted systems
Machine learning involving edge / fog

## Slide 22: CAREM: Context-aware Radio Resource Management
17

## Slide 23: 3
Management of computing resources under dynamic service load

## Slide 24: Use Case: Digital Twin
Digital Twin app
Interface
Coordinates
Commands
EDGE NETWORK
Drivers
Motion planning
Control
RAN
VNF 2
target latency: 60 ms
VNF 1 target latency: 600 ms

## Slide 25: Service scaling out/in
Measure CPU consumption: if above threshold, then scale out:
      A new VM running VNF2 is instantiated, and the workload can be split between the different instances
Is a simple thresholding algorithm enough?

## Slide 26: A ML Approach: An Example
Random Forest classification model
  Input: current Instantiation Level (IL) and average per-VNF CPU load
  Output: IL to apply
Model training and inference model creation
19
ave. CPU load
current no. of VNF instances
Classification Model
suitable no. of VNF instances

## Slide 27: System architecture and operational flow
5GROWTH
Service
Orchestrator
SLA manager
AI/ML Platform
YARN cluster manager
Spark
Interface Manager
BigDL
Ray
MLlib
AI/ML model register
AI/ML param. register
HDFS dataset storage
ML lifecycle Mng
5GROWTH Vertical-oriented Monitoring System
Infrastructure
VM
VM
Logical Links
5GROWTH Vertical Entry Point
5GROWTH Resource Layer
Kafka
Model execution
Monitoring manager
Vertical
Monitoring job configuration
Topic configuration
Real-time
perf. metrics
AIML model request/response
Physical Links
3
4
5
6
7
8
Data consumption
Interface for model onboarding
1
AIML model upload and training
Service request
2
20

## Slide 28: Deployed Scenario
VNF
5Gr-RL
5Gr-VS
WIM
5Gr-SO
Monitoring
5Growth MANO and Monitoring
Model Execution
Barcelona
Torino
Scaling operation
Heterogeneous WAN transport network
VNF
VNF
VIM
Scaling operation
VPN (data, control and management)
AI/ML Platform
YARN cluster manager
Spark
Interface Manager
BigDL
Ray
MLlib
AI/ML model register
AI/ML param. register
HDFS dataset storage
ML lifecycle Mng
Interface for model onboarding

## Slide 29: ML at the edge is indeed effective in controlling/exploiting the heterogeneity of mobile networks at best
Demo
23
https://www.youtube.com/watch?v=7V3AKSrWzzY
Demo at IEEE NFV-SDN 2020 (Best demo award) and at INFOCOM 2021

## Slide 30: Take-away Messages
- Edge: need it and actually works! - AI-driven, fully automatic management of e2e slices: using the most suitable resources from the cloud to the UE, for complex services and heterogeneous vRANs
- It works even under dynamic conditions

## Slide 31
Thank you for your attention!